## Slide 1
The Bear Creek Watershed Association protects & restores water & environmental quality within the Bear Creek Watershed from the effects of land use.

## Slide 2
Operational Bear Creek Watershed 2017

## Slide 3
100 Stream Monitoring Sites
Bear Creek Reservoir
  Inflow Turkey Creek
  Inflow Bear Creek
  Outflow Site 45
  Site 90 input Barr/Milton
Evergreen Lake
Summit Lake (Mt Evans)
Other WQ Features

## Slide 5
100 Monitoring Sites

## Slide 6: 2017 Estimates Recreation Use BCW
Recreational Users Bear Creek Park > 600,000
People Traveling to Mt. Evans > 185,000
Wilderness Access > 25,000
Users Denver Mountain Parks > 225,000
Users Evergreen Lake > 300,000
Jefferson County Open Space > 80,000
Attendees & Visitors Red Rocks/Morrison >1.3 million
Bear Creek Park Swim Beach Use > 750 per weekend
Fishing > 65,000 people per year
BCWA Fact Sheet 35 Recreational Uses in BCW
BCW Total Species | 
Common Sport Fish | Other Reported Fish
16 | 14

## Slide 7: BCWA 2017 Watershed Plan
Online Decision Support Program
Electronic Online Watershed Plan
  36 Policies
  59 Fact Sheets
  22 Data Masters
  34 Informational Maps
  26-yrs of Rulemaking & Standards
  31 Program Documents
  >100 linked reports & documents
  18 Wastewater Management Summaries
  + Other Informational, Methods, Program Guidance, Technical Series, Special Studies, Annual Monitoring Plans
Photo Library
Quarterly Newsletter (>350)
NPS education
Membership special programs

## Slide 9: 2017 Annual Report
WQCC Summary
  Status of Water Quality (Normal Year)
  Status of WQ Goals & Standards (Temperature)
  Phosphorus Trading Program (3 trade policies)
Bear Creek Watershed Association Program

## Slide 10
Average seasonal total phosphorus of 61.8 µg/L in BCR exceeds the 22.2 µg/L goal-standard
Average seasonal chlorophyll-a of 22.5 µg/L was over the 12.2 µg/L standard
Trophic status of the reservoir remains at the Eutrophic-Hypertrophic boundary based on Carlson and Walker indices
Seasonal average reservoir temperature (-1/2-2m) = 20.0oC with no exceedances of the WAT or DM
Lake aeration maintained dissolved oxygen levels (-1/2-2m) at or above 6.0 mg/L throughout most of the growing season
Late season blue-green algal blooms
Recreational fishing remained active

## Slide 17
 | 2017 Total Phosphorus Loading (Pounds) |  |  |  | 
 | Total TP Load | PS | %PS | NPS | %NPS
Turkey Creek Drainage | 1,292 | 84 | 1.4% | 1,208 | 93%
Bear Creek Drainage | 4,742 | 1,007 | 16.7% | 3,734 | 79%
Discharged into Reservoir | 6,034 | 1,092 | 18.1% | 4,942 | 82%
Site 45 Outflow BCR | 3,051 |  |  |  | 
BCR Total Phosphorus Deposition | 2,983 |  |  |  | 
Site 90 - Lower Bear Creek | 2,081 |  |  |  | 

## Slide 21
Bear Creek Watershed Wastewater Treatment Plants by Drainage Basin | WQCC Adopted Phosphorus WLA Pounds/ year | 2017 Discharged Phosphorus Pounds/year | % Allocation Used by WWTF
Bear Creek Drainage |  |  | 
Jefferson County Schools – Mt. Evans Outdoor Lab | 20 | 4.76 | 24%
Brook Forest Inn1 | 5 | 22 | 440%
Evergreen Metropolitan District | 1,500 | 250.73 | 17%
West Jefferson County Metro District | 1,500 | 268.33 | 18%
Kittredge Sanitation and Water District | 240 | 47.39 | 20%
Genesee Water and Sanitation District | 1,015 | 318.67 | 31%
Forest Hills Metropolitan District | 80 | 21.35 | 27%
Town of Morrison | 600 | 74.19 | 12%
Bear Creek Total | 4,960 | 1,007.42 | 20%
Turkey Creek Drainage |  |  | 
Conifer Metropolitan District | 40 | 3.7 | 9%
Conifer Sanitation Association | 40 | 0.95 | 2%
Aspen Park Metropolitan District | 40 | 6.9 | 17%
Jefferson County Schools - Conifer High School | 110 | 3.9 | 4%
Geneva Glen2 | 5 | 19.96 | 399%
Bear Creek Development Corp. - Tiny Town3 | 5 | Hauling Columbia | 
Turkey Creek Total | 240 | 35.41 | 15%
Total Operational Facilities Lbs./year | 5,200 | 1,042.83 | 20%
Reserve Pool4 | 55 | 0 | 0%
Total Phosphorus Wasteload lbs./year | 5,255 |  | 
1-Brook Forest Inn - Compliance Advisory, Reported Effluent Violation Notice of Significant Non-Compliance by WQCD. Exceeded phosphorus concentration limits and pounds as reported by WQCD. No compliance action by WQCD enforcement section. |  |  | 
2-Geneva Glen - Compliance Agreement. Exceeded phosphorus concentration limits and pounds as reported to WQCD. New LAMP in progress. No compliance action by WQCD enforcement section. |  |  | 
3-Records from Columbia Sanitary show they hauled 131,400 gallons in the 2017 operation season |  |  | 
4- The reserve pool in the Control Regulation is 2 pounds of total phosphorus, the 55 pounds listed by the BCWA includes pounds from closed treatment facilities (Singing River Ranch (30), The Fort Restaurant (18), Bear Creek Cabins (5)) |  |  | 

## Slide 23
Segment | Cold-season |  | Warm Season | 
Segment 3 | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 0 | 15 | 0 | 0
% Compliance | 100% | 94% | 100% | 100%
Segment 1a | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 3 | 10 | 0 | 0
% Compliance | 94% | 97% | 100% | 100%
Segment 1d | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances |  |  | 0 | 0
% Compliance |  |  | 100% | 100%
Segment 1e | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 1b | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 0 | 1 | 0 | 0
% Compliance | 100% | 99% | 100% | 100%
Segment 5 | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 6a | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 0 | 1 | 0 | 0
% Compliance | 100% | 99% | 100% | 100%
Segment 6b | 9 oC WAT | 13 oC DM | 17 oC WAT | 21.2 oC DM
# Exceedances | 0 | 0 |  | 
% Compliance | 100% | 100% |  | 
Segment 2 | 13.7°C WAT | 14.3°C DM | 27.5°C WAT | 28.6°C DM
# Exceedances | 0 | 0 | 0 | 1
% Compliance | 100% | 100% | 100% | 100%
Segment 1c | 9°C WAT | 13°C DM | 23.3°C WAT | 23.8°C DM
# Exceedances | 2 | 0 | 0 | 0
% Compliance | 0% | 100% | 100% | 100%

## Slide 24: Adaptive Management Program
Nonpoint source loading & tracking
Coyote Gulch - Trading
Septic Systems – Kerr & Cub
Tracking management practices
Zoning and planning reviews for BMPs
Local presentations, education programs
Flood restoration practices
Assist land-owners
Assist invasive species programs
Green Infrastructure projects
Wildfire assessment
Source water protection
Tributary loading studies
Erosion Control Reviews
Online adaptive management
Climate Modeling

## Slide 25: Coyote Gulch
2006-2017
Trade Pounds = 80.4

## Slide 27
WQCD Station ID | BCWA Station ID | Location | Biotype | MMI |  |  |  |  |  |  | 
 |  |  |  | 2009 | 2010 | 2011 | 2012 | 2014 | 2015 | 2016 | 2017
5756a | 15a | BCLP @ bridge | Transition |  |  |  |  | 66.4 | 59.1 | 67.0 | 56.4
122 | 14a | Morrison @ Gage | Transition | 69.8 | 80.5 | 74.5 | 72.9 | 48.8 | 73.5 | 72.0 | 63.9
122C | 13a | Idledale | Transition | 62.1 | 69.8 | 57.1 | 68.0 | 59.3 | 59.2 | 50.0 | 62.2
122a | 12 | Lair O’ Bear | Transition | 58.5 | 62.2 | 56.4 | 51.3 | 49.5 | 72.2 | 46.0 | 62.9
122b | 9 | O’ Fallon | Transition | 53.6 | 57.7 | 45.5 | 49.9 | 44.8 | 59.1 | 57.0 | 60.1
5762 | 8b | BCC @ Bridge | Transition | 55.6 | 39.1 | 51.1 | 44.3 | 49.6 | 62.3 | 59.0 | 57.4
5763 | 5 | Little Bear | Transition | 52.3 | 56.6 | 42.9 | 40.0 | 56.2 | 68.9 | 75.0 | 38.4
5764 | 3a | Keys @ bridge | Mountain | 38.6 | 36.9 | 45.3 | 46.9 | 43.9 | 63.6 | 37.0 | 57.9
5768d | 2a | Golden Willow | Mountain |  |  |  | 71.9 | 60.8 | 56.6 | 65.0 | 58.1
5768c | 58 | Mt Evans Wilderness | Mountain |  |  | 55.5 | 72.5 | 67.0 | 53.8 | 67.0 | 75.6
BCWA90 | 90 | Wadsworth | Transition |  |  |  |  |  |  | 55.0 | 39.9

## Slide 30
BCWA spent 2.2 million on regulation directed programs
1.3 million on data & monitoring efforts
28-years of data & studies to support good science
>2 million on water quality improvement projects
Discharger members have spent >21 million dollars on WWTFs
BCWA has 78.5 years worth of voluntary efforts
WQCD enforcement staff stated the monitoring provisions of Regulation #74 are not enforceable.
WQCD enforcement staff stated the nonpoint source provisions of Regulation #74 are not enforceable.