## Slide 1
The Bear Creek Watershed Association protects & restores water & environmental quality within the Bear Creek Watershed from the effects of land use.

## Slide 2
Operational Bear Creek Watershed 2019

## Slide 3
105 Stream Monitoring Sites
Bear Creek Reservoir
  Inflow Turkey Creek
  Inflow Bear Creek
  Outflow Site 45
  Site 90 input Barr/Milton
Evergreen Lake
Summit Lake (Mt Evans)
Other WQ Features

## Slide 5
105 Monitoring Sites

## Slide 6: 2018 Estimates Recreation Use BCW
Recreational Users Bear Creek Park > 675,000
People Traveling to Mt. Evans > 188,000
Wilderness Access > 25,000
Users Denver Mountain Parks > 250,000
Users Evergreen Lake > 300,000
Jefferson County Open Space > 80,000
Attendees & Visitors Red Rocks/Morrison >1.3 million
Bear Creek Park Swim Beach Use > 750 per weekend
Fishing > 65,000 people per year
BCWA Fact Sheet 35 Recreational Uses in BCW
BCW Total Species | 
Common Sport Fish | Other Reported Fish
16 | 14

## Slide 7: BCWA 2018 Watershed Plan
Online Decision Support Program
Electronic Online Watershed Plan
  37 Policies
  64 Fact Sheets
  25 Data Masters
  34 Informational Maps
  27-yrs of Rulemaking & Standards
  36 Program Documents
  >100 linked reports & documents
  18 Wastewater Management Summaries
  + Other Informational, Methods, Program Guidance, Technical Series, Special Studies, Annual Monitoring Plans
Photo Library
Quarterly Newsletter (>350)
NPS education
Membership special programs

## Slide 8
Members & Participants | Wastewater Discharger | 2018 Participation
Counties |  | 
Jefferson County |  | Active
Clear Creek County |  | Active
City and Towns |  | 
City of Lakewood |  | Active
Town of Morrison | Yes | Active
Water & Sanitation Districts |  | 
Aspen Park Metropolitan District | Yes | Active
Conifer Sanitation Association | Yes | Dues Paid, Not Active
Evergreen Metropolitan District | Yes | Active
Forrest Hills Metropolitan District | Yes | Active
Genesee Water & Sanitation District | Yes | Active
Geneva Glen | Yes | Dues Paid, Not Active
Jefferson County School District | Yes | Active
Kittredge Water & Sanitation District | Yes | Active
Tiny Town Foundation, Inc. | Yes | Not Paid, Not Active
West Jefferson County Metropolitan District | Yes | Active
Other Member |  | 
Denver Water Department |  | Active
Denver Heath |  | Attended
Participant Agencies |  | 
U.S. Army Corps of Engineers |  | Attended
Jefferson Conservation District |  | Active
WQCD |  | Attended
ETU |  | Active

## Slide 9: 2018 Annual Report
WQCC Summary
  Status of Water Quality (Normal Year)
  Status of WQ Goals & Standards (Temperature)
  Phosphorus Trading Program (3 trade policies)
Bear Creek Watershed Association Program

## Slide 10
Average seasonal total phosphorus of 61.8 µg/L in BCR exceeds the 22.2 µg/L goal-standard
Average seasonal chlorophyll-a of 16.4 µg/L was over the 12.2 µg/L standard
Trophic status of the reservoir remains at the Eutrophic-Hypertrophic boundary based on Carlson and Walker indices
Seasonal average reservoir temperature (-1/2-2m) = 21.4oC with exceedances of the WAT (32) and DM (86)
Lake aeration maintained dissolved oxygen levels (-1/2-2m) at or above 6.0 mg/L throughout most of the growing season
Late season blue-green algal blooms
Recreational fishing remained active
Chart: Chlorophyll-a Bear Creek Reservoir
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Chlorophyll, ug/L | 1.25 | 15.45 | 5.9 | 1.5 | 8.15 | 2.4 | 8.925 | 19.025 | 15.975 | 37.95 | 41.45 | 44.5
Chlorophyll Standard | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2

## Slide 14
Chart: Average Total Phosphorus Watershed
| Site 36 | Site 37 | Site 58 | Site 2a | Site 3a | Site 25 | Site 4a | Site 5 | Site 8a | Site 9 | Site 12 | Site 13a | Site 14a | Site 26 | Site 64 | Site 32 | Site 34b | Site 15a | Site 19 | Site 18 | Site 16a | Site 40a | Site 45 | Site 90 | Evans | Upper Bear | Tribs | EGL | Middle Bear Creek | Upper Tribs | Mt. V | BCP | Turkey | Turkey | BCR | Lower Bear | Seg 7 | Seg 1a | Seg 3 | Seg 1d | Seg 1e | Seg 5 | Seg 4a | Seg 1b | Seg 6b | Seg 6a | Seg 1c | Seg 2
T Phos Ug/l | 3.75 | 8.5 | 7.6667 | 11.5 | 17.8333 | 20.6667 | 27.3333 | 34.5 | 58.5 | 38 | 43 | 47.8333 | 62 | 37.5 | 66.5 | 130.6667 | 15.8333 | 56.1667 | 76 | 45.8333 | 36.8333 | 39 | 41.1667 | 31

## Slide 15
Chart: Total Nitrogen Pounds
| Site 16a-Turkey Creek Inflow | Site 15a-Bear Creek Inflow
Total Nitrogen Pounds | 2705.8714 | 15543.5518

## Slide 16
Chart: Average Total Nitrogen Watershed
| Site 36 | Site 37 | Site 58 | Site 2a | Site 3a | Site 25 | Site 4a | Site 5 | Site 8a | Site 9 | Site 12 | Site 13a | Site 14a | Site 26 | Site 64 | Site 32 | Site 34b | Site 15a | Site 19 | Site 18 | Site 16a | Site 40a | Site 45 | Site 90 | Evans | Upper Bear | Tribs | EGL | Middle Bear Creek | Upper Tribs | Mt. V | BCP | Turkey | Turkey | BCR | Lower Bear | Seg 7 | Seg 1a | Seg 3 | Seg 1d | Seg 1e | Seg 5 | Seg 4a | Seg 1b | Seg 6b | Seg 6a | Seg 1c | Seg 2
TN Ug/l | 191.25 | 315.25 | 193.1667 | 160.3333 | 176.3333 | 95.3333 | 318.8333 | 284.3333 | 662.8333 | 474.6667 | 847.6667 | 588.6667 | 643.8333 | 339.1667 | 519.1667 | 1078.6667 | 762.1667 | 962.5 | 353 | 466 | 615.6667 | 665.8333 | 752.1667 | 898.6667

## Slide 17
 | 2018 Total Phosphorus Loading (Pounds) |  |  |  | 
 | Total TP Load | PS | %PS | NPS | %NPS
Turkey Creek Drainage | 75 | 39 | 52.2% | 36 | 48%
Bear Creek Drainage | 666 | 951 | 142.7% | -285 | -43%
Discharged into Reservoir | 741 | 990 | 133.6% | -249 | -34%
Site 45 Outflow BCR | 409 |  |  |  | 
BCR Total Phosphorus Deposition | 332 |  |  |  | 
Site 90 - Lower Bear Creek | 747 |  |  |  | 
NPS load increase between 45 and 90 | 45% | 338 |  |  | 

## Slide 18
Chart: Chlorophyll-a Bear Creek Reservoir
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Chlorophyll, ug/L | 1.25 | 15.45 | 5.9 | 1.5 | 8.15 | 2.4 | 8.925 | 19.025 | 15.975 | 37.95 | 41.45 | 44.5
Chlorophyll Standard | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2

## Slide 19
Chart: Phytoplankton Seasonal Biovolume um3/ml
| Bluegreen | chrysophyte | Diatom | Green
 | 181401.6198 | 143144.8005 | 56417.6351 | 18720.7771
Functional Group | Species | Seasonal Ave Density #/ml | Seasonal Ave Biovolume, um3/mL
Bluegreen | 5 | 315 | 181,402
chrysophyte | 5 | 463 | 143,145
Diatom | 39 | 59 | 56,418
Green | 6 | 70 | 18,721

## Slide 20
Chart: 
| May | Jun | Jul | Aug | Sep | Oct
Total Phosphorus, Pounds/month | 0.77878 | 1.0236 | 0.88498 | 1.5262 | 0.7284 | 0.65352
Chart: EGL Total Nitrogen Loading
| May | Jun | Jul | Aug | Sep | Oct
Total Nitrogen, Pounds/month | 16.0711 | 12.3804 | 12.5666 | 12.751 | 10.5764 | 6.4045
Chart: EGL Chlorophyll a
| May | Jun | Jul | Aug | Sep | Oct
Chlorophyll a Average | 1.2 | 3.35 | 11.65 | 33.15 | 3.15 | 2.55

## Slide 21
Bear Creek Watershed Wastewater Treatment Plants by Drainage Basin | WQCC Adopted Phosphorus WLA Pounds/ year | 2018 Discharged Phosphorus Pounds/year | % Allocation Used by WWTF
Bear Creek Drainage |  |  | 
Jefferson County Schools – Mt. Evans Outdoor Lab | 20 | 2.68 | 13%
Brook Forest Inn1 | 5 | 0 | 0%
Evergreen Metropolitan District | 1,500 | 297.46 | 20%
West Jefferson County Metro District | 1,500 | 313.18 | 21%
Kittredge Sanitation and Water District | 240 | 40.27 | 17%
Genesee Water and Sanitation District | 1,015 | 226.32 | 22%
Forest Hills Metropolitan District | 80 | 28.57 | 36%
Town of Morrison | 600 | 42.35 | 7%
Bear Creek Total | 4,960 | 950.83 | 19%
Turkey Creek Drainage |  |  | 
Conifer Metropolitan District | 40 | 0.73 | 2%
Conifer Sanitation Association | 40 | 1.85 | 5%
Aspen Park Metropolitan District | 40 | 3.5 | 9%
Jefferson County Schools - Conifer High School | 110 | 1.9 | 2%
Geneva Glen2 | 5 | 31.16 | 623%
Bear Creek Development Corp. - Tiny Town3 | 5 | Hauling Columbia | 
Turkey Creek Total | 240 | 39.14 | 16%
Total Operational Facilities Lbs./year | 5,200 | 989.97 | 19%
Reserve Pool4 | 55 | 0 | 0%
Total Phosphorus Wasteload lbs./year | 5,255 |  | 
1-Brook Forest Inn - Under Compliance Advisory, Still permitted with no reported flow |  |  | 
2-Geneva Glen - Under Compliance Agreement. Concentration and poundage exceedances from May to October 2018 |  |  | 
3-Records from Columbia Sanitary show they hauled 64,700 gallons in the 2018 operation season to South Platte Renewal Partners formally known as Englewood/Littleton WWTP. No Phosphorus Data Taken. |  |  | 
4- The reserve pool in the Control Regulation is 2 pounds of total phosphorus, the 55 pounds listed by the BCWA includes pounds from closed treatment facilities (Singing River Ranch (30), The Fort Restaurant (18), Bear Creek Cabins (5)) |  |  | 

## Slide 22
Chart: BCR Temperature C (0.5-2m)
| 43108 | 43143 | 43178 | 43199 | 43234 | 43262 | 43290 | 43297 | 43319 | 43325 | 43353 | 43369 | 43388 | 43409 | 43444
site 40 | 4.43 | 4.05 | 6.72 | 9.53 | 15.63 | 18.93 | 22.78 | 23.45 | 22.2 | 22.5 | 19.45 | 18.08 | 10.84 | 8.9 | 2.94
Site 41 | 4.3 | 3.55 | 7.08 | 9.53 | 15.85 | 19.13 | 22.9 | 23.15 | 22.33 | 22.68 | 19.7 | 18.15 | 10.9 | 8.9
Site 42 | 4.43 | 7.08 | 9.5 | 15.5 | 18.95 | 22.9 | 23.14 | 22.3 | 22.68 | 19.65 | 18.12 | 10.86 | 8.9
S(Jan-Mar) | 9 | 9 | 9
S(Apr-Dec) | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3

## Slide 23
Segment | Cold-season |  | Warm Season | 
Segment 3 | 9°C WAT | 13°C DM | 17°C WAT | 21.2°C DM
# Exceedances | 4 | 24 | 0 | 5
% Compliance | 82% | 79% | 100% | 96%
Segment 1a | 9°C WAT | 13°C DM | 17°C WAT | 21.2°C DM
# Exceedances | 9 | 64 | 2 | 18
% Compliance | 76% | 76% | 95% | 94%
Segment 1d | 9°C WAT | 13°C DM | 18.2°C WAT | 23.8°C DM
# Exceedances |  |  | 32 | 0
% Compliance |  |  | 50% | 100%
Segment 1e | 9°C WAT | 13°C DM | 19.3°C WAT | 23.8°C DM
# Exceedances | 0 | 0 | 11 | 31
% Compliance | 100% | 100% | 93% | 97%
Segment 1b | 9°C WAT | 13°C DM | 19.3°C WAT | 23.8°C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 5 | 9°C WAT | 13°C DM | 18.2°C WAT | 23.8°C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 6a | 9°C WAT | 13°C DM | 18.2°C WAT | 23.8°C DM
# Exceedances | 0 | 0 | 7 | 0
% Compliance | 100% | 100% | 88% | 100%
Segment 6b | 9°C WAT | 13°C DM | 17°C WAT | 21.2°C DM
# Exceedances | 1 | 8 | 0 | 0
% Compliance | 95% | 94% | 100% | 100%
Segment 2 | 13.7°C WAT | 14.3°C DM | 27.5°C WAT | 28.6°C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 1c | 9°C WAT | 13°C DM | 23.3°C WAT | 23.8°C DM
# Exceedances | 0 | 0 | 13 | 86
% Compliance | 100% | 100% | 92% | 92%

## Slide 24: Adaptive Management Program
Nonpoint Source Loading & Tracking
Coyote Gulch - Trading
Septic Systems – Kerr & Cub
Tracking Management Practices
Zoning And Planning Reviews For BMPs
Local Presentations, Education Programs
Flood Restoration Practices
Assist Land-owners
Assist Invasive Species Programs
Green Infrastructure Projects
Wildfire Assessment
Source Water Protection
Tributary Loading Studies
Erosion Control Reviews
Online Adaptive Management
Climate Modeling

## Slide 25: Coyote Gulch
2006-2018
Trade Pounds = 78.3

## Slide 27
Chart: Total Nitrogen & Phosphorus Seasonal Averages
| All Fens | Control Fen | Northern Fens
Total Nirogen, ug/l | 269 | 99 | 331
Total Phosphorus, ug/l | 171.2045 | 18.4545 | 222.1212

## Slide 28
Chart: Dissolved Copper, Pounds/Month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Site 14a | 5.0217 | 4.2334 | 3.8567 | 4.1049 | 9.3153 | 3.3824 | 5.1138 | 3.0465 | 3.4472 | 3.6286 | 4.5455 | 3.9839
Site 87/34b | 0.14513 | 0.1905 | 0.27117 | 0.17738 | 0.50887 | 0.22679 | 0.46752 | 0.1694 | 0.068036 | 0.11663 | 0.10691 | 0.07633
Site 14c | 4.8065 | 4.1941 | 5.5038 | 4.8805 | 15.6678 | 3.674 | 1.6568 | 3.1938 | 2.762 | 3.4893 | 4.4548 | 3.5755

## Slide 29
BCWA spent $2.2 million on regulation directed programs
$1.35 million on data & monitoring efforts
29-years of data & studies to support good science
>$2 million on water quality improvement projects
Discharger members have spent >$21 million on WWTFs
BCWA has 79.5 years worth of voluntary efforts