## Slide 1
The Bear Creek Watershed Association protects & restores water & environmental quality within the Bear Creek Watershed from the effects of land use.

## Slide 2
Operational Bear Creek Watershed 2019

## Slide 4
105 Stream Monitoring Sites
Bear Creek Reservoir
  Inflow Turkey Creek
  Inflow Bear Creek
  Outflow Site 45
  Wadsworth Site 90 input Barr/Milton
Evergreen Lake
Summit Lake (Mt Evans)
Other WQ Features

## Slide 5: BCWA 2018 Watershed Plan
Online Decision Support Program
Electronic Online Watershed Plan
  37 Policies
  69 Fact Sheets
  27 Data Masters
  36 Informational Maps
  28-yrs of Rulemaking & Standards
  39 Program Documents
  >100 linked reports & documents
  18 Wastewater Management Summaries
  + Other Informational, Methods, Program Guidance, Technical Series, Special Studies, Annual Monitoring Plans
Photo Library
Quarterly Newsletter (>350)
NPS education
Membership special programs

## Slide 6
Average seasonal total phosphorus of 61.8 µg/L in BCR exceeds the 22.2 µg/L goal-standard
Average seasonal chlorophyll-a of 16.4 µg/L was over the 12.2 µg/L standard
Trophic status of the reservoir remains at the Eutrophic-Hypertrophic boundary based on Carlson and Walker indices
Seasonal average reservoir temperature (-1/2-2m) = 21.4oC with exceedances of the WAT (32) and DM (86)
Lake aeration maintained dissolved oxygen levels (-1/2-2m) at or above 6.0 mg/L throughout most of the growing season
Late season blue-green algal blooms
Recreational fishing remained active
Chart: Chlorophyll-a Bear Creek Reservoir
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Chlorophyll, ug/L | 1.25 | 15.45 | 5.9 | 1.5 | 8.15 | 2.4 | 8.925 | 19.025 | 15.975 | 37.95 | 41.45 | 44.5
Chlorophyll Standard | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2

## Slide 7
 | 2018 Total Phosphorus Loading (Pounds) |  |  |  | 
 | Total TP Load | PS | %PS | NPS | %NPS
Turkey Creek Drainage | 75 | 39 | 52.2% | 36 | 48%
Bear Creek Drainage | 666 | 951 | 142.7% | -285 | -43%
Discharged into Reservoir | 741 | 990 | 133.6% | -249 | -34%
Site 45 Outflow BCR | 409 |  |  |  | 
BCR Total Phosphorus Deposition | 332 |  |  |  | 
Site 90 - Lower Bear Creek | 747 |  |  |  | 
NPS load increase between 45 and 90 | 45% | 338 |  |  | 

## Slide 8
Chart: Chlorophyll-a Bear Creek Reservoir
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Chlorophyll, ug/L | 1.25 | 15.45 | 5.9 | 1.5 | 8.15 | 2.4 | 8.925 | 19.025 | 15.975 | 37.95 | 41.45 | 44.5
Chlorophyll Standard | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2 | 12.2

## Slide 9: Adaptive Management Program
Nonpoint Source Loading & Tracking
Coyote Gulch - Trading
Septic Systems – Kerr & Cub
Tracking Management Practices
Zoning And Planning Reviews For BMPs
Local Presentations, Education Programs
Flood Restoration Practices
Assist Land-owners
Assist Invasive Species Programs
Green Infrastructure Projects
Wildfire Assessment
Source Water Protection
Tributary Loading Studies
Erosion Control Reviews
Online Adaptive Management
Climate Modeling