## Slide 1: Bear Creek Watershed Association
The Bear Creek Watershed Association protects & restores water & environmental quality within the Bear Creek Watershed from the effects of land use.
Bear Creek Association Newsletter
Flood Recovery
BCWA PINNACLE

## Slide 2
Bear Creek Watershed 2014

## Slide 3: 2014 Estimates of Recreation Use Bear Creek Watershed
Recreational Users Bear Creek Park > 580,000
People Traveling to Mt. Evans > 177,000
Users Denver Mountain Parks > 225,000
Users Evergreen Lake > 275,000
Attendees & Visitors Red Rocks/Morrison >1.3 million
Bear Creek Park Swim Beach Use > 750 per weekend
Fishing > 65,000 people per year
BCWA Fact Sheet 35 Recreational Uses in BCW

## Slide 4
Members & Participants | Wastewater Discharger | 2014 Participation
Counties |  | 
Jefferson County |  | Active
Clear Creek County |  | Active
City and Towns |  | 
City of Lakewood |  | Active
Town of Morrison | Yes | Active
Water & Sanitation Districts |  | 
Aspen Park Metropolitan District | Yes | Active
Bear Creek Cabins | Yes | Active
Brook Forest Inn | Yes | Active
Conifer Sanitation Association | Yes | Dues Paid, Not Active
Conifer Metropolitan District | Yes | Dues Paid, Not Active
Evergreen Metropolitan District | Yes | Active
Forrest Hills Metropolitan District | Yes | Active
Genesee Water & Sanitation District | Yes | Active
Geneva Glen | Yes | Dues Paid, Not Active
Jefferson County School District | Yes | Active
Kittredge Water & Sanitation District | Yes | Active
Singing River Ranch | Yes | Dues Not Paid, Not Active
The Fort Restaurant | Yes | Active
Tiny Town Foundation, Inc. | Yes | Dues Paid, Not Active
West Jefferson County Metropolitan District | Yes | Active
Other Member |  | 
Denver Water Department |  | Active
Participant Agencies |  | 
Denver Health/ Parks & Recreation |  | Attended
Evergreen Trout Unlimited |  | Active
U.S. Army Corps of Engineers |  | Attended
WQCD |  | Attended

## Slide 5: 2014 Annual Report
WQCC Summary
  Status of Water Quality (Flood Recovery)
  Status of WQ Goals & Standards (Temperature)
  Phosphorus Trading Program (3 trade policies)
Bear Creek Watershed Association Program
Chart: Total Phosphorus Pounds/Season
| Site 37 | Site 58 | Site 2a | Site 3a | Site 25 | Site 5 | Site 8a | Site 9 | Site 12 | Site 13a | Site 14a | Site 34 | Site 35 | Site 50 | Site 64 | site 32 | Site 18 | Site 19 | Seg 7 | Seg 1a | Seg 3 | Seg 1e | Seg 4a | Seg 5 | Seg 6a | Seg 6b
T Phos Pounds | 70 | 105.7804 | 506.8095 | 1638.0557 | 84.4974 | 2276.7981 | 2613.8335 | 2504.3676 | 2671.4357 | 2664.8554 | 3275.1647 | 80.6361 | 391.0124 | 1073.1647 | 87.1001 | 319.4381 | 95.536 | 127.0294

## Slide 6: TN Data
Chart: Total Nitrogen Pounds/ Season
| Site 37 | Site 58 | Site 2a | Site 3a | Site 25 | Site 5 | Site 8a | Site 9 | Site 12 | Site 13a | Site 14a | Site 34 | Site 35 | Site 50 | Site 64 | site 32 | Site 18 | Site 19 | Seg 7 | Seg 1a | Seg 3 | Seg 1e | Seg 4a | Seg 5 | Seg 6a | Seg 6b
TN pounds | 200.2374 | 4870.4979 | 6841.9281 | 11527.8171 | 1074.1414 | 16597.9567 | 20843.4005 | 20321.7002 | 22896.5174 | 24587.062 | 25806.0391 | 4013.1456 | 1588.3611 | 6981.1024 | 984.888 | 3161.582 | 1479.0224 | 1776.231

## Slide 7: 2014 BCR Internal Load Problem
Chart: Total Phosphorus Deposition in Bear Creek Reservoir
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
BCR Total Phosphorus Deposition | 667 | 1014 | 1395 | 223 | 374 | 6759 | 2081.82

## Slide 8: Reservoir Hydrology
Chart: 2014 Reservoir Inflow [Ac-Ft Per Month]
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Turkey Creek Inflow | 1106.514 | 264.5322 | 183.8043 | 666.288 | 2846.1999 | 196.317 | 242.8184 | 377.7516 | 186.2037 | 276.6285 | 155.8638 | 92.2095
Bear Creek Inflow | 922.095 | 1610.196 | 1106.514 | 1963.17 | 5839.935 | 5354.1 | 2704.812 | 2766.285 | 1546.74 | 1702.8021 | 521.1324 | 307.9797
Total Inflow | 2028.609 | 1874.7282 | 1290.3183 | 2629.458 | 8686.1349 | 5550.417 | 2947.6304 | 3144.0366 | 1732.9437 | 1979.4306 | 676.9962 | 400.1892

## Slide 9: Watershed Hydrology
Chart: 
| 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014
USGS 06710385 BEAR CREEK ABOVE EVERGREEN, CO | 40315.3815 | 28517.523 | 44513.3925 | 29168.9385 | 21713.85 | 23812.8555 | 31267.944 | 23957.6145 | 16285.3875 | 17515.839 | 46178.121 | 22582.404 | 35104.0575 | 51027.5475 | 46250.5005 | 18022.4955 | 18746.2905 | 7961.745 | 24464.271 | 23740.476 | 27793.728 | 14186.382 | 40822.038 | 18963.429 | 18384.393 | 20121.501 | 14910.177 | 11797.8585 | 33801.2265 | 33801.2265

## Slide 10: Total Phosphorus Loading
2014 Total Phosphorus Loading (Pounds) |  |  |  | 
 | Total TP Load | PS | NPS | %NPS
Turkey Creek Drainage | 489 | 7 | 482 | 99%
Bear Creek Drainage | 3,521 | 1,069 | 2,452 | 56%
Discharged into Reservoir | 4,010 | 1,076 | 2,934 | 63%
Site 45 Outflow BCR | 1,980 |  |  | 
BCR Total Phosphorus Deposition | 2,031 |  |  | 

## Slide 11: Chlorophyll Trends
Chart: Chlorophyll-a Bear Creek Reservoir
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Chlorophyll, ug/L | 4.85 | 2.4 | 2.4 | 1.95 | 6.95 | 3.5 | 11.55 | 9.15 | 4.15 | 4.1 | 1.85 | 1.95

## Slide 12: Evergreen Lake Dredging
Chart: 
| 41773 | 41806 | 41827 | 41871 | 41897 | 41918
Chlorophyll a | 1.5 | 1.2 | 7.7 | 5.9 | 3.2 | 1.8

## Slide 13: Summit Lake and upper Bear Creek
Data demonstrates pollution source(s) causing elevated nutrient loads, low pH conditions and reduced dissolved oxygen
Repaired new toilet vaults
Plume diminishing
Reduced Total Phosphorus average 216 ug/l
Reduced Total Nitrogen average 377 ug/l

## Slide 14: Wastewater Management
Bear Creek Watershed Wastewater Treatment Plants by Drainage Basin | WQCC Adopted Phosphorus WLA Pounds/ year | 2014 Discharged Phosphorus Pounds/year | % Allocation Used by WWTF
Bear Creek Drainage |  |  | 
Jefferson County Schools – Mt. Evans Outdoor Lab | 20 | 6.36 | 32%
Brook Forest Inn | 5 | 1.4 | 28%
Evergreen Metropolitan District | 1,500 | 286.52 | 19%
West Jefferson County Metro District | 1,500 | 384.56 | 26%
Kittredge Sanitation and Water District | 240 | 71.31 | 30%
Genesee Water and Sanitation District | 1,015 | 251.98 | 25%
Forest Hills Metropolitan District | 80 | 23.55 | 29%
Town of Morrison | 600 | 40.9 | 7%
Bear Creek Total | 4,960 | 1,066.6 | 22%
Turkey Creek Drainage |  |  | 
Conifer Metropolitan District | 40 | Land Applied | 0%
Conifer Sanitation Association | 40 | 1.7 | 4%
Aspen Park Metropolitan District | 40 | 4.4 | 11%
Jefferson County Schools - Conifer High School | 110 | 1.05 | 1%
Geneva Glen1 | 5 | Land Applied | 0%
Bear Creek Development Corp. - Tiny Town2 | 5 | Hauling Columbia | 0%
The Fort3 | 18 | No Monitoring | 0%
Turkey Creek Total | 258 | 7.2 | 3%
Total Operational Facilities Lbs/year | 5,218 | 1,073.73 | 21%
Reserve Pool | 37 | 0 | 0%
Total Phosphorus Wasteload lbs/year | 5,255 |  | 
1-Geneva Glen treatment system land applies, no Reported Pounds |  |  | 
2-Records from Columbia Sanitary show they hauled 72,400 gallons in the 2014 operation season |  |  | 
3-Permit; No established monitoring |  |  | 

## Slide 15: BCWA 2014 Watershed Plan
Online Decision Support Program
Electronic Watershed Plan (10.8 GB)
  35 Policies
  51 Fact Sheets
  18 Data Masters
  34 Informational Maps
  + Informational, Methods, Program Guidance, Technical Series, Reports
  Photo Library (>18 GB)
Quarterly Newsletter (>300)
Increased NPS education
Membership special programs

## Slide 16: Bear Creek Reservoir & Park

## Slide 18: Reservoir/ Lake Studies
Bear Creek Reservoir
  Inflow Turkey Creek
  Inflow Bear Creek
  Outflow site 45 (input Barr/Milton Watershed
Evergreen Lake
Summit Lake

## Slide 19: Coyote Gulch
2006-2014
Trade Pounds = 92.2
Chart: Total Phosphorus
| 2006-2007 | 2007-2008 | 2009* | 2010* | 2011* | 2012 | 2013 | 2014 | Pre-construction | Post-Construction
T Phos | 19.9588 | 4.429 | 6.6654 | 8.1264 | 6.0778 | 2.7461 | 4.6 | 4.4

## Slide 20: Bear Creek Watershed Association Surface Water Monitoring Program Version 2014.01
Annually reviewed and updated

## Slide 21: Sampling Begins at the Top

## Slide 22: Watershed Monitoring
82 Monitoring Sites

## Slide 23: Monitoring Program Elements
Water quality monitoring program
  82 Sites (some monitored since 1991)
    5 Bear Creek Reservoir monitoring profiles
    Evergreen Lake profiles
    Physical, Chemistry & Biology
Year round temperature monitoring of Bear Creek and Turkey Creek
  >2,750,000 measurements
Monitor total phosphorus, dissolved phosphorus, nitrate+nitrite, total ammonia, total nitrogen, TIN, oxygen, specific conductance, temp, carbon, pH, bacteria, phytoplankton, zooplankton, chlorophyll, Secchi, TSS
Special Studies
  Fishery surveys at 12 sites
  Macroinvertebrate collections
  Habitat
  Flow studies
  BMP Effectiveness
  Stormwater data collection
  E. Coli
  Septic Systems Contributions
  Lake Sediments

## Slide 24: BCR Temperature Compliance
Chart: BCR 2014 Temperature C (0.5-2m)
| 41645 | 41680 | 41724 | 41750 | 41778 | 41806 | 41827 | 41849 | 41855 | 41869 | 41890 | 41897 | 41932 | 41961 | 41981
site 40 | 2.65 | 2.225 | 6.625 | 11.475 | 12.025 | 16.175 | 20.3 | 20.325 | 19.05 | 19.5 | 17.725 | 15.975 | 9.3 | 3.2 | 2.4
Site 41 | 2.625 | 1.875 | 6.925 | 11.925 | 12.525 | 16.1 | 20.25 | 20.25 | 18.925 | 19.575 | 17.875 | 15.875 | 12.025 | 3.25 | 2.525
Site 42 | 1.825 | 6.825 | 11.525 | 12.125 | 16.1 | 20.2 | 20.375 | 18.975 | 19.65 | 17.825 | 16.075 | 11.8 | 3.1 | 2.5
Site 43 | 2.06 | 2.26 | 6.82 | 11.6 | 12.84 | 16.68 | 20.62 | 20.46 | 19.28 | 19.5 | 17.8 | 16.16 | 11.94 | 3 | 2.52
Site 44 | 2.425 | 1.675 | 6.35 | 11.55 | 13.025 | 16.5 | 20.575 | 20.575 | 19.2 | 19.6 | 17.875 | 15.975 | 11.85 | 3.2 | 2.6
S(Jan-Mar) | 9 | 9 | 9
S(Apr-Dec) | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3 | 23.3
Segment 1c Datalogger Temperature Summary 2014 |  |  |  |  |  |  |  | 
All Temperatures in C | 30-Min Temp. COLD/WARM SEASON |  | Nov 1-Mar 31 Stream Std. WAT (9C) | Nov 1-Mar 31 2-Hr Avg. Temp. | Nov 1-Mar 31 Stream Std. DM (13C) | Apr 1-Oct 31 Stream Std. WAT (19.3C) | Apr 1-Oct 31 2-HR Avg. Temp. | Apr 1-Oct 31 Stream DM (23.8C)
Min | 6.36 | 2.53 |  | 6.42 | 6.94 | 6.01 | 2.84 | 3.88
Max | 8.22 | 21.72 |  | 8.10 | 8.10 | 20.75 | 21.49 | 21.49
Avg | 7.12 | 15.00 |  | 7.12 | 7.51 | 15.03 | 15.00 | 15.40
Measurements | 480 | 22222 |  | 120 | 10 | 66 | 5554 | 462
# 9C WAT exceeded |  |  |  |  |  |  |  | 
% Compliance WAT |  |  |  |  |  |  |  | 
# 13C DM exceeded |  |  |  | 0 |  |  |  | 
% Compliance DM |  |  |  | 100% |  |  |  | 
# 23.3C WAT exceeded |  |  |  |  |  | 0 |  | 
% Compliance WAT |  |  |  |  |  | 100% |  | 
# 23.8C DM exceeded |  |  |  |  |  |  |  | 0
% Compliance DM |  |  |  |  |  |  |  | 100%

## Slide 25: Watershed Temperature Compliant
 | Cold-season |  | Warm Season | 
Segment 3 | 9C WAT | 13C DM | 17C WAT | 21.2C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 1a | 9C WAT | 13C DM | 17C WAT | 21.2C DM
# Exceedances | 0 | 1 | 0 | 0
% Compliance | 100% | 99% | 100% | 100%
Segment 1d | 9.0°C WAT | 13.0°C DM | 18.2C WAT | 23.8C DM
# Exceedances |  |  | 0 | 0
% Compliance |  |  | 100% | 100%
Segment 1e | 9C WAT | 13C DM | 19.3C WAT | 23.8C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 1b | 9C WAT | 13C DM | 19.3C WAT | 23.8C DM
# Exceedances | 6 | 14 | 0 | 0
% Compliance | 67% | 90% | 100% | 100%
Segment 5 | 9C WAT | 13C DM | 18.2C WAT | 23.8C DM
# Exceedances | 4 | 17 | 0 | 0
% Compliance | 88% | 79% | 100% | 100%
Segment 6a | 9C WAT | 13C DM | 18.2C WAT | 23.8C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 6b | 9C WAT | 13C DM | 17C WAT | 21.2C DM
# Exceedances | 0 | 1 | 0 | 0
% Compliance | 100% | 99% | 100% | 100%
Segment 2 | 13.7°C WAT | 14.3°C DM | 27.5°C WAT | 28.6°C DM
# Exceedances | 0 | 0 | 0 | 0
% Compliance | 100% | 100% | 100% | 100%
Segment 1c | 9C WAT | 13C DM | 24.0°C WAT | 26.0°C DM
# Exceedances |  | 0 | 0 | 0
% Compliance |  | 100% | 100% | 100%

## Slide 26: Active Nonpoint Source Management
Coyote Gulch - Trade Poundage Allocation
Septic Systems – Kerr & Cub
Tracking management practices
Fourteen zoning and planning reviews for BMPs
>22 local presentations, education programs
Assist invasive species programs
Green Infrastructure projects
Wildfire assessment & source water protection
Erosion Control Reviews

## Slide 27: Replaced BCR Aeration System

## Slide 28: Kerr/ Swede Gulch
E. coli Summary, Geometric Mean |  |  |  |  |  |  |  |  | 
BCWA Site | 2010 | 2011 |  |  |  |  |  |  | 
 | May-Dec | J-D (Annual) | Jan-Feb | Mar-Apr | May-Jun | Jul-Aug | Sep-Oct | Nov-Dec | May-Oct
 | n=36 | n=48 | n=8 | n=8 | n=8 | n=8 | n=8 | n=8 | n=24/6
Sites 52-53 |  |  | 14 | 2 | 6 | 5 | 6 | 2 | 6
Site 52 - Confluence | 10 | 6 |  |  |  |  |  |  | 15
Site 53 - Riefenberg | 13 | 4 |  |  |  |  |  |  | 9
Site 54 - Kerr | 16 | 5 |  |  |  |  |  |  | 3
Site 55 - Swede | 11 | 3 |  |  |  |  |  |  | 2
 |  | 2012 |  |  |  |  |  |  | 
Sites 52-53 |  | 5 | 3 | 1 | 11 | 26 | 10 | 3 | 13
Site 52 - Confluence |  | 3 |  |  |  |  |  |  | 6
Site 53 - Riefenberg |  | 4 |  |  |  |  |  |  | 9
Site 54 - Kerr |  | 10 |  |  |  |  |  |  | 32
Site 55 - Swede |  | 3 |  |  |  |  |  |  | 13
 |  | 2013 |  |  |  |  |  |  | 
Sites 52-53 |  | 3 | 2 | 1 | 9 | 14 | 1 | 3 | 5
Site 52 - Confluence |  | 2 |  |  |  |  |  |  | 4
Site 53 - Riefenberg |  | 2 |  |  |  |  |  |  | 5
Site 54 - Kerr |  | 6 |  |  |  |  |  |  | 14
Site 55 - Swede |  | 3 |  |  |  |  |  |  | 3
 |  | 2014 |  |  |  |  |  |  | 
Sites 52-53 |  | 4 | 3 | 2 | 5 | 11 | 5 | 4 | 6
Site 52 - Confluence |  | 3 |  |  |  |  |  |  | 6
Site 53 - Riefenberg |  | 2 |  |  |  |  |  |  | 3
Site 54 - Kerr |  | 8 |  |  |  |  |  |  | 11
Site 55 - Swede |  | 6 |  |  |  |  |  |  | 7

## Slide 29
Chart: Total Trout (Rainbow and Browns) Biomass Mainstem of Bear Creek
| 1988 | 1989 | 1990 | 1991 | 1994 | 1997 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2014
Total Biomass | 535.8 | 514 | 189.9 | 461 | 507 | 295 | 535 | 758 | 629 | 629 | 560 | 529 | 726 | 929 | 618 | 748 | 733 | 778 | 815 | 536
Chart: Total Trout Biomass Bear Creek
| 1991-1999 | 2000-2003 | 2004-2013 | 2014 After Flood
All Data per Year | 2381.5714 | 2486.5 | 6768.25 | 4152
Complete sets (5-sites) | 2448.6667 | 2658.5 | 5645.75 | 2922